## Slide 1
« Gcin’amanzi » : Soweto water supply project
Combining the implementation of the right to water with efficient water use through prepayment

## Slide 2: « Gcin’amanzi » : Soweto water supply project
Situation before project (2005):
  162 000 households/ 1 M. persons
  90% of connections billed on a lump sum basis (20 m3/month vs 61 m3/mois consumption), wastage, deteriorated networks, very high losses and UFW (>80%)
  Revenue collection : 25% , non payment was a political act under apartheid
  Regional water stress: high marginal cost of water
« Gcin’amanzi » (conservation de l’eau) :
  Free installation of prepayment water meters, application of Free Basic Water Supply, Subsidized tariffs, cancellation of customer debts, renewal of public and private networks
  Main risks : i) social acceptance (good), ii) legality

## Slide 3: Lesira-Teq Metering - Overview
  => Jobourg Water was comforted by a judgment of Constitutional Court but this lead to :
  Evolution JW strategy and technology : from prepayment to intelligent water meters
Customer has option of Prepayment, Post paid, Flat rate, or Conventional modes
Customer can change between modes after completing relevant application
Changing between modes (once authorised) is done at vending point using User Tag and Hand Held Vending Unit (HHVU)
Free Basic Water (FBW) and Emergency Water (EW) can be available in all modes
Meter can be locked at any time
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 4: 1. Prepayment mode
Customer buys credit in advance from vending point
When credit is finished, meter goes to restricted flow of 40l/h. More credit must be purchased
Customer receives Free Basic Water (FBW) of 9 000 litres once per month or 300 liters per day (50 l. per person per day)
Emergency Water (EW) is available up to four times per year (1 000 litres per occasion) but only when there is no credit and FBW is finished

## Slide 5: 2. “Post paid” mode
When FBW is finished, water will continue
The user/client chooses his assigned negative credit limit in litres or Rand value.
This amount can be consumed over a number of months
The meter shows the “Debt” water total in volume and in Rand
Full flow will be maintained until the negative credit limit is reached. Then the meter will turn into a restricted flow mode of 40l/h (optional)
Customer receives Free Basic Water (FBW) of 9 000 litres once per month or 300 litres per day and Emergency water

## Slide 6: Lesira-Teq Metering - Overview